ASPECTS OF THE NON-HOLONOMIC SYSTEMS’ DYNAMICS

Nicolae Pandrea, Nicolae-Doru Stănescu

University of Piteşti, Piteşti, ROMANIA, e-mail: nicolae_pandrea37@yahoo.com

University of Piteşti, Piteşti, ROMANIA, e-mail: s_doru@yahoo.com

Abstract: This paper presents a few aspects of the systems’ motion with non-holonomic constraints. We treat the cases of one or two non-holonomic constraints for a material point and, also, the cases of one or more non-holonomic constraints for the rigid body. In the paper are also presented applications to the concerned subjects.

Keywords: non-holonomic constraints, dynamics, systems, stability

1. INTRODUCTION

Further on, we shall discuss some aspects of the mechanical systems’ motion subjected to non-holonomic constraints.

2. MATERIAL POINT’S DYNAMICS SUBJECTED TO NON-HOLONOMIC CONSTRAINTS

2.1. General aspects

An example of non-holonomic constraint for the material point is the case in figure 1 where the point  describes the plane following curve of the point , which has determined motion ; .

Figure 1: The material point with a non-holonomic constraint.

If we denote by the speed of the point , one obtains the relations

| , | (1) |
| --- | --- |

where

|  | (2) |
| --- | --- |

and from here results the non-holonomic constraint given by the relation

| . | (3) |
| --- | --- |

In the case of the motion of the material point  on a curve in the three dimensional space, from the relations as (1), one obtains two non-holonomic constraints defined by the relations

| ; . | (4) |
| --- | --- |

Generally, the non-holonomic constraints of the material point will be considered in the form

| , | (5) |
| --- | --- |

where , , ,  are functions of , , , .

2.2. The motion of the material point subjected to one non-holonomic constraint

A. General case

If the material point of mass  is acted by the force

|  | (6) |
| --- | --- |

and it is subjected to the non-holonomic constraint

| , | (7) |
| --- | --- |

where , ,  are the versors of the co-ordinates axes, and , , , , , ,  are functions of , , , , then the differential equations of the motion are

| ; ; , | (8) |
| --- | --- |

being a parameter that must be determined.

Deriving the relation (7) with respect to the time and using the notations:

| ; , | (9) |
| --- | --- |
| , | (10) |

ones obtain the expression

|  | (11) |
| --- | --- |

where from with the aid of the expressions (8), we deduce the function

| . | (12) |
| --- | --- |

To utilize the fourth order Runge-Kutta method to integrate the moving equations, one uses the notations:

| ; ; , , ; | (13) |
| --- | --- |

and e or she obtains the first order system

| ; ; ; ; ; . | (14) |
| --- | --- |

In a numerical application, if we consider ,  and the non-holonomic constraint

| , | (15) |
| --- | --- |

we obtain in order

| ; ; ; | (16) |
| --- | --- |

and system (8) becomes

| ; ; . | (17) |
| --- | --- |

Considering the initial conditions which satisfy the relation (15)

| , | (18) |
| --- | --- |

one obtains the solution

| ; ; . | (19) |
| --- | --- |

B. The theorem of the kinetic energy and mechanical work

Multiplying the relations (8) by , , and , respectively, summing and keeping into account the expression of the elementary mechanical work,

| , | (20) |
| --- | --- |

one deduces the expression

|  | (21) |
| --- | --- |

which can be also written as

| , | (22) |
| --- | --- |

where  is the kinetic energy,

| . | (23) |
| --- | --- |

Expression (22) defines the theorem of the kinetic energy and mechanical work for the case of one non-holonomic constraint. In the case when  and the force  is conservative,

| , | (24) |
| --- | --- |

where  represents the potential, one deduces the expression of the mechanical energy conservation

| . | (25) |
| --- | --- |

2.3. The motion of the material point subjected to two non-holonomic constraints

If the non-holonomic constraints are

| ; , | (26) |
| --- | --- |

then ones obtain the differential equations system

| ; ; . | (27) |
| --- | --- |

Utilizing now the notations:

| ; , | (28) |
| --- | --- |
| , | (29) |

by derivation with respect to the time, one deduces the expressions:

| ; | (30) |
| --- | --- |

and hence, from (27), (30), with the aid of the relations:

| ; ; , | (31) |
| --- | --- |

we deduce the expressions:

| ; . | (32) |
| --- | --- |

To numerical integration of the differential equations (26) with the parameters ,  given by relations (32), we make the notations (13) and results the first order system

| ; ; ; ; ; . | (33) |
| --- | --- |

Analogously, for the theorem of the kinetic energy and mechanical work, one obtains the expression

| . | (34) |
| --- | --- |

In a numerical application, if we consider the non-holonomic constraints

| ; , | (35) |
| --- | --- |

we obtain in order the expressions:

| ; ; ; ; ; ; ; ; | (36) |
| --- | --- |

and results, in the absence of the force , for mass , the differential equations:

| ; ; | (37) |
| --- | --- |

which, with the initial conditions that satisfy the relations (35):

| , | (38) |
| --- | --- |

have the solution

| ; ; . | (39) |
| --- | --- |

2.4. Determining the following curve

Let us consider the point  of mass , acted by the force  (fig. 2), which moves such that its speed  passes through the point  with determined motion ; ; . The equations of motion for the point  in the case of the non-holonomic constraints (4) are:

| ; ; . | (40) |
| --- | --- |

Figure 2: The following curve.

It also follows

| ; ; ; ; ; | (41) |
| --- | --- |

and we obtain the system (33), where ,  are given by the relations (32).

If the force  is conservative, then and from the relation (34) one deduces the speed  as a function of the speed  and the initial position , specifically

| . | (42) |
| --- | --- |

From the equalities

| , | (43) |
| --- | --- |

where

| , | (44) |
| --- | --- |

we obtain the differential equations

| ; ; , | (45) |
| --- | --- |

which can be numerical integrated with the initial conditions:

| ; ; ; ; ; ; ; ; . | (46) |
| --- | --- |

In a numerical application, we consider

| ; ; ; | (47) |
| --- | --- |

and results the system (45) where

| ; ;. | (48) |
| --- | --- |

The numerical integration leads to the set of values from the table 1.

Table 1: The results of the numerical integration.

| 0 | 0 | 0 | 0 | 16 | 0 | 0 | 4.000 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0,05 | 1,486 | 0,047 | 0,036 | 19,551 | 1,186 | 0,890 | 4.086 |
| 0,1 | 2,042 | 0,1017 | 0,076 | 7,350 | 1,120 | 0,840 | 4.183 |
| 0,15 | 2,339 | 0,162 | 0,121 | 4,880 | 1,287 | 0,966 | 4.287 |
| 0,2 | 2,550 | 0,230 | 0,173 | 3,697 | 1,453 | 1,090 | 4.403 |
| 0,25 | 2,716 | 0,307 | 0,230 | 2,980 | 1,609 | 1,207 | 4.529 |
| 0,3 | 2,852 | 0,391 | 0,293 | 2,490 | 1,755 | 1,316 | 4.664 |
| 0,35 | 2,967 | 0,482 | 0,362 | 2,131 | 1,894 | 1,421 | 4.805 |
| 0,4 | 3,067 | 0,580 | 0,435 | 1,855 | 2,027 | 1,520 | 4.953 |
| 0,45 | 3,154 | 0,685 | 0,514 | 1,634 | 2,153 | 1,615 | 5.106 |
| 0,5 | 3,231 | 0,795 | 0,597 | 1,453 | 2,276 | 1,707 | 5.263 |
| 0,55 | 3,300 | 0,912 | 0,684 | 1,302 | 2,393 | 1,795 | 5.423 |
| 0,6 | 3,361 | 1,035 | 0,776 | 1,173 | 2,507 | 1,880 | 5.587 |
| 0,65 | 3,417 | 1,163 | 0,872 | 1,061 | 2,616 | 1,962 | 5.754 |
| 0,7 | 3,468 | 1,296 | 0,972 | 0,964 | 2,722 | 2,042 | 5.922 |
| 0,75 | 3,514 | 1,435 | 1,076 | 0,878 | 2,824 | 2,118 | 6.091 |
| 0,8 | 3,556 | 1,578 | 1,184 | 0,801 | 2,922 | 2,192 | 6.262 |
| 0,85 | 3,594 | 1,727 | 1,295 | 0,732 | 3,017 | 2,263 | 6.435 |
| 0,9 | 3,629 | 1,880 | 1,410 | 0,670 | 3,108 | 2,331 | 6.607 |
| 0,95 | 3,661 | 2,038 | 1,528 | 0,614 | 3,195 | 2,396 | 6.780 |
| 1 | 3,690 | 2,199 | 1,650 | 0,564 | 3,278 | 2,459 | 6.954 |

The graphic representations are given in the figures 3, 4 and 5.

From the figures mentioned above and from the table 1 we easily deduce the conclusions: the values of the co-ordinates ,  and  are increasing and tend to the values of ,  and ; excepting  (because  is limited) which tends to zero, the rest of the speeds are increasing, as the module of the speed , too.

Figure 3: Variations ,  and  for .

Figure 4: Variations ,  and  for .

Figure 5: Variation  for .

3. DYNAMICS OF THE RIGID BODY WITH NON-HOLONOMIC CONSTRAINTS

3.1. The case of one non-holonomic constraint

Let us consider the rigid in motion relative to the reference fix frame  and let , ,  be the co-ordinates of the mass center , , ,  the central principal inertial axes, , ,  the Eulerian angles, and , ,  the projections onto the axes , ,  of the angular speed .

The non-holonomic constraint of the rigid is defined by the relation

| , | (49) |
| --- | --- |

where , , , , , ,  are functions of , , , , , , .

The kinetic energy of the rigid body writes in the form

|  | (50) |
| --- | --- |

where  is the mass, , ,  are the principal central inertial moments, and the angular speeds are given by the relations

| ; ; . | (51) |
| --- | --- |

If the rigid is acted at  by the force  and by the moment , then the Lagrange’s equations write in the form

| ; ; , | (52) |
| --- | --- |
| ; ; , | (53) |

where , ,  are the projections of the moment  respectively onto the axis , nodes’ axis and axis. It is easy to prove the existence of the relations:

| ; ; | (54) |
| --- | --- |

and if we use the notations:

| ; ; | (55) |
| --- | --- |

we obtain from (52) and from Euler’s conditions, the equations of motion

| ; ; ; ; ; . | (56) |
| --- | --- |

From the cinematic relations (51) one deduces the expressions:

| ; ; | (57) |
| --- | --- |

and the equations of the non-holonomic constraint, by using the relations

| ; ; | (58) |
| --- | --- |

becomes

| . | (59) |
| --- | --- |

Deriving this relation and using the relation

| , | (60) |
| --- | --- |

one obtains

|  | (61) |
| --- | --- |

and keeping into account the equations (56), one deuces the expression

|  | (62) |
| --- | --- |

To numerical integration, we pass to a first order system using the notations:

| ; ; ; ; ; ; ; ; ; ; ; | (63) |
| --- | --- |

and we obtain the system

| ; ; ; ; ; ; ; ; ; ; ; , | (64) |
| --- | --- |

where  calculates with relation (62), and the initial conditions are:

| ; ; ; ; ; ; ; ; ;; ; ; . | (65) |
| --- | --- |

Based on the calculus relations established above, we can describe the following algorithm for the values ,  and the known functions , …, .

One calculates in order:

– the functions , , , , , ;

– the functions , , , , ,  with relations (55), (58);

– the derivatives ,  with the relations from the set (64);

– the derivatives , , , , , ,  with relations like

| ; | (66) |
| --- | --- |

– the derivatives , ,  with relations

| ; ; ; | (67) |
| --- | --- |

– the functions ,  with the relations (61), (62);

– we integrate the system (64) considering the integration step  of hundredth of second.

3.2. The case of more non-holonomic constraints

Considering the case when the rigid has  non-holonomic constraints in the form

| , , | (68) |
| --- | --- |

using the notations

| ; ; , | (69) |
| --- | --- |

one obtains the matrix equations system

| ; ; ; ; ; . | (70) |
| --- | --- |

This system of equations, with the matrix notations

| ; ; ; ; ; , | (71) |
| --- | --- |

transforms in the matrix equation

| . | (72) |
| --- | --- |

Utilizing the notations like (58)

| ; ; | (73) |
| --- | --- |

the non-holonomic constraints (68) with the aid of relations (57) and the notation

|  | (74) |
| --- | --- |

write in matrix form

| . | (75) |
| --- | --- |

Deriving the relation (75) and using the notation

| , | (76) |
| --- | --- |

one obtains the expression

|  | (77) |
| --- | --- |

which, keeping into account the relation (72) becomes

|  | (78) |
| --- | --- |

and from here we obtain the matrix

| . | (79) |
| --- | --- |

Further on, the solution is obtained from the system (72) with  given by the relation (79).

3.3. The rolling of a wheel on plane

Let us consider a wheel of radius  on a horizontal plane (fig. 6), the wheel being homogenous and rolling on this plane.

Figure 6: The model of a wheel on a plane.

We select the fix frame  such that the plane  coincides to the given plane and we select the mobile frame  such that the axes ,  are in the wheel’s plane,  being its center. We shall also consider the system  with the axes parallel to those of the system . It follows that the node axis  is parallel to , the intersection axis between the plane  and the wheel’s plane. In the figure we presented the Euler’s angles:  - the precession angle,  - the proper rotation angle, and  - the nutation angle.

The condition of the rolling without sliding for the wheel on the plane pretends that the speed for the point  of contact between wheel and plane to be zero,

| , | (80) |
| --- | --- |

where we have applied the general Euler relation for the points  and .

Due to the fact that the versor  is orthogonal to  and reads , where ,  and  are the versors of the fix axes, we deduce

| . | (81) |
| --- | --- |

On the other hand, the components , ,  of the vector angular speed on the fix frame’s axis are given by

| ; ; . | (82) |
| --- | --- |

Denoting by , ,  the co-ordinates of the point  relative to the fix reference system, expression (80) leads us to

| ; ; . | (83) |
| --- | --- |

The last relation (83) defines a holonomic constraint because it can be integrated leading to

| . | (84) |
| --- | --- |

Therefore, the system has two non-holonomic constraints (the first and the second relation (83)) and a holonomic constraint in differential form (the third relation (83)) or integral form (expression (84)).

Let us consider that the wheel is acted only by its own weight .

The position of the wheel is defined by the generalized co-ordinates , , , , .

The kinetic energy reads

| , | (85) |
| --- | --- |

the vector  expressed in the system  being given by

| ; ; . | (86) |
| --- | --- |

In addition, ; ;  and we denote .

Results

| . | (87) |
| --- | --- |

The potential energy writes

| . | (88) |
| --- | --- |

The second order Lagrange’s equations, for the case of non-holonomic constraints:

| ; , | (89) |
| --- | --- |

with , , functions of , …,  and , and conservative forces, are in the forma

| ; , | (90) |
| --- | --- |

where  are Lagrange’s multipliers. Ones obtain the expressions

| ; ; ; . | (91) |
| --- | --- |

Replacing the last relation (91) in the third expression (91), we get

| . | (92) |
| --- | --- |

Deriving the first two relations (83) with respect to time and replacing the results in the last, respectively the second relation (91), one obtains the other two Lagrange’s equations:

| , | (93) |
| --- | --- |
| . | (94) |

Denoting now , , , , , , from Lagrange’s equations (92), (93) and (94) ones obtain the six non-linear first order differential equations system

| ; ; ; ; ; . | (95) |
| --- | --- |

The equilibrium positions are determined equating to  the right-hand side terms of the relations (95). Results , ,  and we get the equilibrium positions

| ; ; ; ; ; , | (96) |
| --- | --- |

where ,  are arbitrary real values, and .

Let us now denote by ,  the functions in the right-hand sides of the expressions (95) and by , , .

The characteristic equation , where  is the Jacobi matrix, , and  is the unity six order matrix 6, keeping into account that  for every ,  excepting , ,, , reads

| , | (97) |
| --- | --- |

where from . The characteristic equation (97) has an unique root  with the multiplicity order . For the linear system the equilibrium is unstable, the same thing being true for original non-linear system.

In fact, it can be observed that the theorems of the central manifold can not be applied (there not exists the matrix  which has eigenvalues with negative real parts), and a Liapunov function is hard to be found.

The sentence that the equilibrium is unstable is an immediate corollary of theorem Lejeune-Dirichlet. In fact, we shall prove that the equilibrium position given by the expressions (96), in which due to the symmetry of the wheel we limit ourselves to , the potential energy hasn’t a local minimum. Hence, in accord to the relation (88), we have

| ; ; | (98) |
| --- | --- |

and therefore  has a local maximum at the equilibrium position.

Considering a deviation ,  relative to the solution  of the system (95), one obtains the system in variations

| ; ; ; ; ; | (99) |
| --- | --- |

Let us consider the motion defined by

| ; ; ; ; ; , | (100) |
| --- | --- |

i.e. an uniform rotation around a vertical axis that passes through the contact point between the wheel and plane.

System (99) becomes now

| ; ; ; ; ; . | (101) |
| --- | --- |

Making now the evident approximations

| ; ; ; ; , | (102) |
| --- | --- |

system (101) becomes

| ; ; ; ; ; . | (103) |
| --- | --- |

Deriving the relation before the last relation (103) with respect to the time an keeping into account the last relation (103), one finds the expression

|  | (104) |
| --- | --- |

or

| . | (105) |
| --- | --- |

The motion is stable if

| . | (106) |
| --- | --- |

REFERENCES

[1] Arrowsmith, D., K., Place, C., M., An Introduction to Dynamical Systems, Cambridge University Press, 1994.

[2] Broer, H., W., Krauskopf, B., Vegter, G., (eds.) Global Analysis of Dynamical Systems, Institute of Physics Publishing, Bristol and Philadelphia, 2001.

[3] Carleson, L., Gamelin, T., W., Complex Dynamics, Springer–Verlag, New York, Heidelberg, London, Paris, 1993.

[4] Carr, J., Applications of Centre Manifold Theory, Springer–Verlag, New York, Heidelberg, Berlin, 1981.

[5] Pandrea, N., Chiroiu, V., Stănescu, N.–D., Munteanu, L., Dynamical systems. Theory an Applications, Romanian Academy Publishing House, Bucharest, 2006 (in press).

[6] Curtu, R., Introduction to the theory of dynamical systems, Infomarket Publishing House, Braşov, 2000.

[7] Dumortier, F., Roussarie, R., Sotomayor, J., Żoladek, H., Bifurcations of Planar Vector Fields. Nilpotent Singularities and Abelian Integrals, Springer–Verlag, Berlin, Heidelberg, New York, 1991.

[8] Georgescu, A., Moroianu, M., Oprea, I., Theory of bifurcation. Principles and applications, Publishing House of the University of Piteşti, 1999.

[9] Guckenheimer, J., Holmes, P., Nonlinear Oscillations, Dynamical Systems, and Bifurcation of Vector Fields, Springer–Verlag, New York, Berlin, Heidelberg, London, Paris, Tokyo, Hong Kong, 1983.

[10] Hale, J., K., Koçak, H., Dynamics and Bifurcations, Springer–Verlag, New York, Berlin, Heidelberg, London, Paris, Tokyo, Hong Kong, Barcelona, Budapest, 1991.

[11] Kuznetsov, Y., A., Elements of Applied Bifurcation Theory, Springer–Verlag, New York, Berlin, Heidelberg, London Paris, Tokyo, Hong Kong, Barcelona, Budapest, 1995.

[12] Lurie, A., I., Analytical Mechanics, Springer–Verlag, Berlin, Heidelberg, New York, Barcelona, Hong Kong, London, Milan, Paris, Tokyo, 2002.

[13] Neĩmark, Ju., I., Fufaev, N., A., Dynamics of Nonholonomic Systems, Translations of Mathematical Monographs, vol. 33, American Mathematical Society, Providence, Rhode Island, 1972.

[14] Pandrea, N., Stănescu, N.–D., Mechanics, Didactical and Pedagogical Publishing House, Bucharest, 2002.

[15] Perko, L., Differential Equations and Dynamical Systems, Springer–Verlag, New York, Berlin, Heidelberg, 1996.

[16] Sibirsky, K., S., Introduction to topological dynamics, Noordhoff International Publishing, Leyden, The Netherlands, 1975

[17] Teodorescu, P., P., Mechanical systems. Classical models, vol. IV, Technical Publishing House, Bucharest, 2002.

[18] Voinea, R., Stroe, I., V., Introduction to the theory of dynamical systems, Romanian Academy Publishing House, Bucharest, 2000.

[19] Pandrea, N., On the motion of the material point with non-holonomic constraints, Scientifical Bulletin of the University of Piteşti, series Applied Mechanics, vol. 1, 1995.

# Text boxes

|  | International Workshop (Advanced Researches in Computational Mechanics and Virtual Engineering ( 18 – 20 October 2006, Brasov, Romania |
| --- | --- |