THE STUDY OF SOME NONLINEAR DYNAMICAL SYSTEMS WITH DISTRIBUTED PARAMETERS

M. Lupu1, F. Isaia2

1 “Transilvania” University of Brasov, Brasov, ROMANIA, m.lupu@info.unitbv.ro

2 “Transilvania” University of Brasov, Brasov, ROMANIA, isaiaflorin@yahoo.com

Abstract: In this paper, the oscillations of some nonlinear dynamical systems with specially distributed parameters are studied. The nonlinear part of the equations depends on the speed under polynomial form. Such situations generalize the Van der Pol equations with one, two, three or four parameters. It is the case of the electrical transistorized circuits (Lienard), the Rayleigh equations for nonlinear vibrations in elasticity, the aero-dynamical flutter. Here, besides the elastic force and the harmonic perturbations, we have dumping forces which contain polynomial terms in speed and in this case, the energetic perturbations can generate self-oscillations. For these systems, we study the stability of solutions in the autonomous or non autonomous case, the existence of bifurcations and limit cycles by using the criteria of Hopf and Bendixon and the Liapunov function. By applying the average method or asymptotic developments with respect to the small parameter, the resonance and the self-oscillations for these nonlinear dynamical systems are studied and the trajectories are specified.

Keywords: nonlinear dynamical systems, self-oscillations, stability, bifurcation, limit cycle.

1. INTRODUCTION

In this paper we will study nonlinear equations of the type

,								(1)

where  is a small parameter and  is a nonlinear function in . Particularly, we will deal with equations where the damping force  has variable coefficients which contain polynominals with  of the type [1], [2], [3]

.			(2)

The family of equations (2) is a subset of the so called “Van der Pol” equations (VP). They represent mathematical models for mechanic vibrations, fluid oscillations [5], electrical transistorized circuits, generating lamps [10], flutter oscillations in aerodynamics [7], dampers with friction [9], astronomical phenomena, etc. The forces  can also be harmonic.

Particularly, equations (2) can also be quasilinear:

(3)

or

.									(3’)

From equations of type (3), with the change  and by integration, the Rayleigh equation can be obtained [4], [9]. Another form of (VP) equation is

,									(4)

which represents the self-oscillating motion with dry friction of a rigid body on a driving belt with constant speed [2], [10]. A similar equation is the mathematical model for an aerodynamic flutter activated by the elastic force and the wind which implies a polynominal resistance force [7]:

.									(4’)

A general form of the (VP) equation is [1]

(5)

The study of the stability of solutions is performed by considering the phase space  and by studying the behavior of solutions in the neighborhood of equilibrium points. In fact, we attach to every equation presented bellow, a system of the form

(6)

which is a special case of the systems

.									(6’)

The equilibrium points are the solutions  of the algebraic system with unknowns [4]

.									(7)

Because of nonlinear forces with distributed parameters, there appear perturbations of the stability, bifurcations, limit cycles, self-oscillations. The criteria and the methods used herein are well known: the first approximation, Hopf and Bendixon bifurcations [6], [10], the method of the Liapunov function [4], the Van der Pol method with the method of constants variation, asymptotic approximations (Krilov-Bogoliubov-Mitropolski) [2], [3], [10], resonances, etc.

Now, we exemplify the technique for the choice of the sufficiently small and adimensional parameter  and the obtaining of the quasilinear equation. So, by starting from equation

,

by dividing to , by denoting , , by performing the change  , ,  and by choosing the sufficiently small parameter as the coefficient of , we obtain the notations ,  and the equation

.						(8)

For the other equations, we can similarly proceed in order to choose the parameter.

2. STABILITATY. BIFURCATIONS. SELF-OSCILLATIONS. RESONANCE

We will do this study for the (VP) equations (3), (5), autonomous or non-autonomous [8], [10].

We consider the reduced equation (3) and the corresponding system in the phase space

,										 (9)

.									(10)

The equilibrium point is . The first approximation of system (10) will be

.									(11)

The characteristic polynominal with the corresponding roots will be

.			(12)

If , then  is an asymptotic stable point for the linear system (11) as for the nonlinear system (10). In fact, for ,  is an asymptotic stable node and for ,  is an asymptotic stable focus [2], [4].

If , then  is an unstable point for the linear system (11) as for the nonlinear system (10), the trajectories leaving  when .

If , then  is a simple stable centre for the linear system (11), so we cannot specify the stability of  for the nonlinear system (10). Therefore, we will use the Liapunov and Bendixon theorems in order to study the existence of Hopf bifurcations and stable limit cycles. We will verify the existence of a periodic trajectory in the neighborhood of . The nonexistence of such trajectory can be verified with the Bendixon theorem [1], [10]: The system ,  has a periodic solution if and only if the expression  changes its sign or takes zero value. In the case of system (10), we have  which takes zero value for . So, system (10) admits no periodic solution in the half-plane , in the half-plane  or in the strip  and every periodic solution intersects the straight lines . We also know that if this periodic solution is a stable limit cycle, then it contains the unstable point . For this case we have a Hopf bifurcation [6]: If the characteristic polynominal (12) has complex roots of  type , with ,  for ,  for ,  and , then for  sufficiently small, the system ,  admits a periodic solutions.

Here, ,  for , ,  and hence, for  system (10) admits a periodic solution which is a limit cycle. In order to specify the stability of the limit cycle, we will use the complex form of system (6’). We have , , . By adding the two equations of (6’) we obtain

,									(13)

where  contains monominals of degrees 2, 3 of  [6], [7]

.		(14)

Define the first Liapunov coefficient to be the real number

.			(15)

We also know that . We remind the topological Hopf criterion:

-if , then the periodic solution is a stable limit cycle with supercritical Hopf bifurcation.

-if , then the periodic solution is an unstable limit cycle with subcritical Hopf bifurcation.

In the case of system (10) we have the complex form

.				(16)

For , we have . Therefore, the periodic solution is stable limit cycle which contains the unstable point .

Remark. A different approach of system (10) or equation (16) is the use of polar coordinates: , , . One obtains a system of type ,  which can be qualitatively studied and sometimes integrated . In our case, the system obtained in this manner is nonlinear and difficult.

In order to solve system (10), because of its nonlinearity, we will use the Van der Pol method and the averaging method which is in fact the first approximation from asymptotic methods [8], [10].

We start from equation , where for , we have the solution  . In the following, we will consider that ,  are parameters with slow variation and by using the method of constants variation, we have

,									(17)

,		(18)

Replacing , ,  in that equation, we get

.			(19)

The solution of system (17), (19) with unknowns  is

.								(20)

We consider the polar coordinates

(21)

where ,  have a slow variation in time and we get

.						(22)

Therefore, the solution , with , becomes

.							(23)

By averaging relations (20) with respect to period  and using (21), (22), we obtain

.			(24)

Denoting  and solving (24), we have

.				(25)

When  and  are given, the differential system (25) and the initial conditions ,  allow us to find the amplitude  and the phase difference . Because  and  have a slow variation, system ,  allows us to find the critical points . It is easy to see that  and therefore, the curves  define circles on the plane  which settle the boundaries of some circular annuli of stability or limit cycles. If , then we have instability and if, then we have stability. Indeed, by perturbing the amplitude  in equation

,

we obtain

.

Self-oscillations. They are oscillations produced by the energy transmitted to the system from sources with non-oscillating character: damping or resistance with dry friction, wind, maintained self-induction. Inside the motion equations, damping forces with variable coefficients appear and in certain moments, the characteristic equation admits real positive roots (instead of complex roots) which increase the amplitude. The phenomenon of resonance appears when we have perturbing external forces, while self-oscillations appear because of interaction between internal forces, particularly if these forces depend on speed with high exponents. For example, we have self-oscillations in equations

,

,

if the conditions , respectively , are fulfilled during a short period of time. After this period, the amplitude  satisfy  when , independently of the initial conditions.

Returning to (25), we remark that we have to find  and then we have to determine a limit stationary amplitude , when . The motivation of this operation is that equation  represents the variation of the energy and of the mechanical work produced by the nonlinear terms  of an equation of type . If the mechanical work  is negative during a short period of time, then the energy decreases and the motion is amortized. If the mechanical work is positive during a short period of time, then the energy increases. These two situations do not assure an energetic balance for all periods, therefore the condition for the uniformity of self-oscillations is

.

We find   which verifies  and , when .

By performing this calculation for equation

and using (25), we have

,				(26)

i.e.

.									(27)

By integrating the obtained equations and by using the initial conditions , , we get

(28)

We have  (for ). We remind that ,  and we remark that the straight line  is an asymptotic line for the curves , therefore the oscillations  are tangent to the straight lines  and the regime of motion becomes stationary for oscillations (independently of the initial condition ). We deduce from (28) that the trajectory ,  from the phase space is a spiral line which tend to a stable limit cycle when . This is the ellipse

,

for  in the neighborhood of point . In this point the Hopf bifurcation holds.

The non-autonomous case. Consider equation

.								(29)

By applying the method of Krilov-Bogoliubov-Mitropolski (K-B-M) [2], [3], [5] to equation (29), we seek for an asymptotic solution of type

.							(30)

By replacing (30) in (29) and by making the identification with respect to ,  (the first approximation) we get the following equations

,									(31)

,							(32)

Using the initial conditions , , , , we find for equations (31) the solutions (28) and for the non-homogenous linear equation (32), we find the solution

.						(33)

Remark the term , which results from the homogenous linear equation, the perturbing term  and the term , which is due to the excitation. We also remark that if , then, besides the self-oscillations, we have resonance and hence instability. Remark that by using the linearization and asymptotic theories, the nonlinear terms  can introduce in the final solution harmonic, sub-harmonic or super-harmonic terms which can make a resonance with cu the own oscillation . It is the case of term . These forced appearances request separated solutions [2], [3].

We have  with self-oscillations and , . This means that the elongation is bounded and that we have a simple stability in the point  which is a simply stable centre.

3. THE STUDY OF THE GENERALIZED VAN DER POL EQUATION

We can similarly study the general (VP) equation (8)

which, by the change , , becomes

.

We can directly consider equation

(34)

which, by the change , , becomes

,							(35)

where , , .

We analyze equation (34) for the autonomous case. By considering the phase space for , , we have

,						(36)

with the equilibrium point . The first approximation around  of system (36) is

,								(37)

with the characteristic equation  and roots . The stability of trajectories with respect to  is identical to that from Section 2, systems (10), (11): For , we have asymptotic stability and  for , we have instability.

For , we will study the existence of bifurcations and of limit cycles. The Bendixon-Liapunov theorem states: If the domain  contains the periodic curve ,  with normal vector , if a trajectory , with speed  intersects the curve in some point, then we have

-if , then there is a stable limit cycle;

-if , then there is an unstable limit cycle.

In our case,  (see (36)). It follows that, if , then  inside the circular annulus of radii ,  and so there is a limit cycle inside this circular annulus. The same conclusions can be made by using the Liapunov function .  We have ,  in ,  (see (36)). It follows that  inside the ellipse  with axes , . Hence,   is an unstable point and the domain bounded by the ellipse is a domain of stability for the limit cycle.

Now, we verify the existence of Hopf bifurcations for system (36) and  with the help of the complex form of this system:

.			(38)

By the Hopf criterion (see (15)), we have  which assure the existence of a stable limit cycle in the neighborhood of , . So, there is stable closed trajectory and all trajectories will be spiral lines which will tend to this curve and will leave  which will be an unstable point.

Now, we study equation (35) for the autonomous case with the Van der Pol method and the averaging method as they have been described in Section 2, relations (17)-(25). We start with , where ,  are parameters with slow variation. Performing the calculations, we get

.									(39)

The critical point is

(for ) and is obtained from (39) by writing

.

By solving the first equation of (39) and taking account of the initial condition , we obtain

,							(40)

.							(41)

Note that

.								(42)

For  and  the trajectories  from the phase space are spiral lines which tend, when , to the stable limit cycles  which is an ellipse.

The curve  given by (41) has as wraps lines the straight lines . We also observe the existence of self-oscillations because, by (42), the amplitude  of  increase to  when , independently of . So, the motion tend to an oscillating stable motion in interval .

The non-autonomous case of equation (35) can be treated with the (K-B-M) method as in Section 2. This is the purpose of a future paper.

4. CONCLUSIONS

This paper has a scientific and didactic character by making a study on the class of general Van der Pol equations and by presenting the techniques for the use of the existing mathematical apparatus and by emphasizing the stability, the bifurcations, the self-oscillations and the resonances.

REFERENCES

[1] Bellomo, N.; Preziosi, N.; Romano, A.: Mechanics and Dynamical Systems with Mathematics, Birkhauser, Boston, 2000.

[2] Deciu, E.; Bugaru, M.; Dragomirescu, C.: Vibratii neliniare ca aplicatii in ingineria mecanica, Ed. Acad. Romane, Bucuresti, 2000.

[3] Dinca, F.; Teodosiu, C.: Nonlinear and Random Vibrations, Ed. Acad. Romane, Bucuresti, 1973.

[4] Dragos, L.: Principiile mecanicii analitice, Ed. Tehnica, Bucuresti, 1976.

[5] Georgescu, A.: Aproximatii asimptotice, Ed. Tehnica, Bucuresti, 1989.

[6] Kuznetsov, Y.A.: Elements of Applied Bifurcation Theory, Springer Verlag, New York, 1998.

[7] Lupu, M.; Postelnicu, A.; Deaconu, A.: A Study on the Flutter Stability of Dynamic Aeroelastic Systems, Proceedings CDM 2001 Brasov, 37-46.

[8] Lupu, M.; Isaia, F.: The Study of Some Speed Regulators for Non-Autonomous Vibrating Mechanisms, Bulletin of the “Transilvania” University of Brasov, Vol. 12(47), 2005 (to appear).

[9] Teodorescu, P.P,: Sisteme mecanice, Vol. 4, Ed. Tehnica, Bucuresti, 2002.

[10] Voinea, R.; Stroie, I.:Introducere in teoria sistemelor dinamice, Ed. Acad. Romane, Bucuresti, 2000.

# Text boxes

|  | 1st International Conference (Computational Mechanics and Virtual Engineering ( COMEC 2005 20 – 22 October 2005, Brasov, Romania |
| --- | --- |